TX2 Vehicle Charging Intructions.ppt
AGV4000 Vehicle Charging Instructions.ppt
 Reference: Owner’s Manual UBC41 4-in-1 Battery Charger – Tripp Lite.pdf
CTI One Corporation
Version: x0.1
Date: September 3, 2018
Project Lead: Harry Li, Ph.D.
Team members:
Minh Duc Ong
Company confidential

---
Vehicle Power Nodes
The vehicle has 2 power supply nodes: 36V node and 12V node.
- 36V includes three 12V batteries which are connected in series.
- 12V includes only one 12V batteries
36V power node connects to
- Motors
+
-
-
+
-
-
+
+
12V
12V
12V
12V + 12V + 12V = 36V node
12V power node connects to
- Router,
- TX2 Server1, TX2 Server2.
- LPC node
+
-
-
+
12V
12V node

---
Charging Instructions
Step 1: Turn off the motors and the processors of the vehicle.
Step 2: Disconnect 36V power node from the motors and the processor.
Step 3: Select main AC power outlet. (110V)
Step 4: Set the Low Charge Rate Switch.
Step 5: Connect the power cord’s connector to into the charger’s power inlet. Then plug the other end of power cord into the AC power outlet.
Step 6: Press the Battery Voltage Selection button on the battery charger to be 36V.
Step 7: Connect the charger’s clamps to the battery terminals as following:
Step 7.1: Connect the positive clamp to the battery positive terminal.
Step 7.2: Then connect the negative clamp to the battery negative terminal.
Step 8: After the charging is finished, disconnect the charger from the 36V power node.
Step 9: Reconnect the battery to the motors and the processor.
Note: For the 12V power node, please repeat step 1 to step 9.