CTI One Corporation

CAMSVR-2
User Guide

CTI One Corporation
3679 Enochs Street
Santa Clara, CA 95051

Version: 1.0

Date: Mar.18, 2020
User Guide for CAMSVR-2
CTI One Corporation
2020-03-18	Create this document	YY

# I. Hardware Description

Table 1 is the hardware definition of CAMSVR-2.

## Table 1. Hardware Description
Device	Description	Note
1. Camera	1.1 Resolution 320x240;
2. Connection	2.1 RJ-45 Interface (Cat5e Ethernet Cable)
3. Power Adapter	3.1 Input Power: DC 12V 2A

The hardware description is illustrated in Figure 1.

Figure 1. The hardware definition.

# II. Setup CAMSVR-2
## 2.1. Connect CAMSVR-2 To Host PC
Connect a USB cable to a host PC; Connect Ethernet cable from CAMSVR-2 to the RJ-45 board; Connect a power supply cable to CAMSVR-2, the AI program will start on CAMSVR-2 automatically;

## 2.2. Check USB Interface
### 2.2.1 Open a terminal window
### 2.2.2 Perform below a command to check USB Interface
      ls /dev/tty*
     * Please check ttyUSB*
2.2.3 Change mode of USB interface
     sudo chmod 777 /dev/ttyUSB0
## 2.3. Change USB Port Settings
### 2.3.1 Open camsvr-2/camsvr/settings.py
2.3.2 Change USB_PORT setting to same as 2.2.2
     USB_PORT = '/dev/ttyUSB0'

# III. Operating Guide
## 3.1. Start Web Server
### 3.1.1 Move to the web server dirctory
Perform below command;
      cd camsvr-2

3.2.2 Start Web Server
     For running the server, perform the following command;
      python3 manage.py runserver 0.0.0.0:8080

      The server will start running.
## 3.2. Access to Web User Interface
### 3.2.1 Access to Web User Interface
1. Start your browser(Chromium), and enter http://127.0.0.1:8080 then hit a enter/return key, you should be directed to the starting page. See Figure 3.2.1

Figure 3.2.1 Web Server and UI Interface.
## 3.3. Intrusion Detection
### 3.3.1 Intrusion Detection
        1. Click Intrusion Detection in the side menu, it will show the window of Intrusion Detection as Figure 3.3.1;

Figure 3.3.1 The window of Intrusion Detection

3.3.2 Draw a rectangle
1. In the window of Intrusion Detection, click any 2 points to draw rectangle (Not do dragging), a rectangle in green line will show as Figure 3.3.2;
(Current version Web Server does NOT show a rectangle and change picture)

Figure 3.3.2 The rectangle in the window of Intrusion Detection

3.3.3 Detect Illegal Intrusion
1. When Illegal Intrusion is detected, The system will display a detected frame as Figure 3.3.3;
(Current version Web Server shows a previous frame that is sent by CAMSVR-2)

Figure 3.3.3 Detected Frame

# Appendix A. Software List
Name	Version
Ubuntu	16.04
Python	3.5.2
Chromium	53.0.2785.143

# Appendix B. Python Package List
Name	Version	Name	Version
Django	2.1.2	numpy	1.15.2
OpenCV	3.4.2.16	goto-statement	1.2
pyserial	3.4

(END)